## Slide 1: Dynamic ‘Slice’ Spectrum Sharing
Ravi Ravindran
(June 1st , 2021)

## Slide 2: Problem
A Network Slice is a composition of 5G RAN, Core and Transport layer functions to meet a service’s SLA requirements.
The RAN itself is composed of a combination of CU-CP, CU-UP, DU and RU functions.
The user plane functions in CU-UP, DU and RU can be engineered to cater to different slice types
  E.g. the PDCP/RLC/MAC/PHY layer features can be engineered to offer very low latency and high reliability required for URLLC PDUs
However, considering the cost of spectrum, this resource is expected to be shared among the different slice types.
Static or Semi-static mode of resource management could lead to low spectral utilization.

## Slide 3: Problem
Joint scheduling is a difficult problem, schedulers optimized for one type of traffic is easier but tradeoff utilization.
  With URLLC complex Pre-emption/Puncturing and DCI notification is required and Embb HARQ is affected requiring re-transmission
  This invention tries to improve utilization while keeping the simplicity of keeping separate schedulers while allowing real-time interaction
  Significant literature addressing this
Disjoint scheduling
  In this approach, the DUs managing different slice traffic could interact in near real-time to exchange slice level traffic statistics with other DUs and agree on a spectrum resource sharing considering the Priority among of the different slices.
  DSS operates at the RAT level, here we exploit this idea at the slice level among DUs
The invention solves the problem of enabling multiple DU handling different Slice traffic (e.g. PODs in the same server) to interact in realtime and agreeing on a PRB resource distribution using the algorithm proposed in the invention.
The algorithm can also be operated in a centralized manner

## Slide 4: System View (with Disjoint Scheduling)
DU
(EMBB)
DU(URLLC)
CU-UP
CU-CP
UPF
DU (mmtc)
DNN
RU
Slice-x
Slice-y
Slice-z
We assume different types of UEs being served by multiple DUs (e.g implemented as PODs in the same physical server)
The spectrum resources are also shared among the DUs and its UEs in the cell
Multiple slices with different SLA requirements are being served
DRBs are set up between CU/DU to transfer user data in the UL/DL.
The Data DRBs are routed through the same RU, in a way that the resources are orthogonally shared among the UEs.
URLCC users have low latency 3-9ms RAN delay requirement and 10-4 PER requirement, hence these mission critical flows have highest priority in the system.
DU Server

## Slide 5: Key Idea – System View
F1-Ap/RLC Buffers
F1
UL/DL PRB Resource Management
MAC DL/UL Schedular
CQI
F1-Ap/RLC Buffer
UL/DL PRB Resource Mgmt + PRB Mgmt. Algorithm
MAC DL/UL Schedular
Traffic Estimator
DU (URLLC)
PHY
PHY
Traffic Estimator
F1
EMbb DRBs
URLLC DRBs
CQI
Slice Policy
Slice Policy
[PRB Reservation]
SON (Slice Manager)
DU (Embb)

## Slide 6: System - Functional Details
Traffic estimator interfaces with the MAC function and estimates the average arrivals across DRB/UE over X*TTIs.
  This can be aggregated over the active UEs to determine the total arrivals across X*TTI.
TE also estimates total DL buffer occupancy across all the UEs in the DU
The UL/DL PRB resource mgmt. function, uses the Average Arrival/Buffer packet statistics from the TE and maps it to equivalent PRB level statistics considering UE channel conditions and the target BLER.
The global Slice Policy is shared across DUs and has information related to the type of slice work in the other DUs and the policies related to resource sharing,
  e.g. X% of total PRB resources can be reserved for eMBB/MMTC so that they are not starved
The URLLC DU has the highest priority in terms of resource reservation, but shouldn’t exceed the aggregate policy requirements of other lower priority DRB

## Slide 7: PRB Estimation Algorithm
Two level slices, URLLC has the highest priority and the remaining slices are considered equal
The resource PRB reservation can be synced among DUs every X TTIs
The DU handling the URLLC traffic is the master node. The other DUs (EMBB and MMTC) shares its PRB requirement every X TTIs with DU(URLLC)
Every X TTIs the DU(URLLC) executes the following steps, the results is applied at the to + X*TTI:
Master DU
[URLLC]
DU
[EMBB]
DU
[MMTC]
[Embb PRB Requirment]
[URLLC PRB Filter]
[MMTC PRB Requirement]
t0
t0
t0
DU URLLC
DU Embb
DU MMTC
to + X*TTI
Embb(Arrival Rate, Buffer)
PRB(URLLC)
Mmtc(Arrival Rate, Buffer)
PRBfilter(Embb)
PRBfilter(Mmtc)

## Slide 8: DL/UL PRB Estimation Algorithm
S1. Every X*TTIs, , the DU(URLLC) calculates Average arrival and Buffer status in terms of PRB, using TE , CQI from the UEs, and the BLER that is to be achieved. DU(URLL) is aware of the policy PRB requirements for Embb and MMTC, PRBp (EMBB), PRBp (MMTC)
S2: Every X*TTIs, DU(Embb) DU(MMTC) shares their corresponding Average Arrival Rate and Buffer Statistics in terms of PRB with DU(URLLC)
S3: At the DU(URLLC), Geometric smoothing over arrival rate along with a simple system evolution equation can be used to predict the PRBe (URLLC), PRBe (EMbb), PRBe (mmtc), or Other estimation/prediction techniques (AI/ML) can be used predict future demand every X TTIs,
  PRBe(URLLC) = f(, PRB_Burst(URLLC) },
  PRBe(Embb= ,
  PRBe(MMTC)= ,
S4. If the (TotalPRB - PRBe (URLLC) ) > (PRBe (embb) + PRBe (mmtc) ) (i.e, total of the estmiates is less than the capacity)
  Then the master DU (URLLC) notifies the PRB filter to the other DUs, and this is used for the next X TTI
  Separate PRB filters will be used to indicate what will be used by the DU[urllc], DU[Embb], and DU[mmtc]
S5. Else if the (Residual PRB) < (PRBe [embb] + PRBe[ mmtc] )
  Determine the PRB estimates as follows, PRBe(URLLC) = Total PRB – max (PRBp (EMBB) + PRBp (MMTC), ResidualPRB), where ResidualPRB = TotalPRB - PRBe (URLLC)
  Divide the max(PRBp (EMBB) + PRBp (MMTC), ResidualPRB)) in proportion to PRBe (embb) and PRBe(mmtc)
  Separate PRB filters will be used to indicate what will be used by the DU(urllc), DU(Embb), and DU(mmtc)
S6: The DU (URLLC) communicates the PRB filter and shares it with the DU (embb) and DU(mmtc) instances.
S7. If the DU(MMTC) or DU(Embb) has service degradation with current slice policy, it can be communicated to the NMS to increase their slice share, this will be a non-realtime optimization
 The algorithm can be applied for UL PRB estimation and management as well using the Buffered Statistics from the UEs, which is processed by the DUs and shared with the DU(URLLC)

## Slide 9: Generalized Scenario
vCU
vCU
DU Server
URLLC
URLLC
URLLC
MMTC
MMTC
EMBB
EMBB
Master
URLLC
Leadar
EMBB
Leader
MMTC
Sub- MMTC
Sub- MMTC
Sub- URLLC
Sub- URLLC
Sub- EMBB
Sub- EMBB
[PRB Reservation]
[PRB Reservation]
A leader can be selected among the same type of slice DUs
The leader DU aggregates the requirements from other similar DUs
The previous algorithm now works among the elected leaders
The URLLC DU acts as the unit that makes decision on
Sub- URLLC

## Slide 10: RIC Based Solution
In this framework, there is a Slice-RM XApp in the Near-RT RIC.
The XApp’s subscribe to DRB level statistics such as Arrival Rate, Buffer Data for the DU (URLLC, Embb, MMTC) in terms of PRB
The XApps then uses the Total PRB capacity information, along with current demand for URLLC and other slices , and the slice policy to decide the PRB allocation in the next X*TTI
PRB estimation algorithm in Slide 8 can be executed by the XApp
The X*TTI now has to account for the communication delay between the delay
One benefit with RIC based approach is, non-RAN metrics such as location, UE mobility pattern can be taken into account while estimating the future PRB allocations.
Near-RT RIC
(Slice RM –Xapp)
Non-RT RIC
vCU
DU[URLLC]
DU[Embb]
DU[MMTC]
E2
E2
E2
E2
F1
UPF
A1
Traffic Estimator
UL/DL PRB Resource Management
Near-RT RIC
Slice RM (Xapp)
Slice Policy
E2
RLC/MAC
DRBs
DU (URLLC)
A1
E2
E2
Slice PRB Estimation Algo.
t0
t0
t0
Xapp (Slice RM)
DU (URLLC)
DU (EMBB)
to + X*TTI
PRBfilter (MMTC)
PRB(URLLC)
t0
DU (MMTC)
PRBfilter (MMTC)
PRBFilter(MMTC)

## Slide 11: PRB Estimation Algorithm

## Slide 12: PRB Estimation Algorithm
verage arrival over X TTIs in PRBs at time n
: Buffer size in PRBs at nth reporting instance
A : Allocation to be used for (n+1)th time instance over X*TTI
X*TTI
TE
PRB Mgmt.
PRB Mgmt .+ Algo.
X*TTI
TE
X*TTI
PRB Mgmt.
,,
,,
Slice Policy
n
t0
t0
DU URLLC
DU Embb
DU MMTC
n+1
Embb(Arrival Rate, Buffer)
Mmtc(Arrival Rate, Buffer)
PRBfilter(Embb)
PRBfilter(Mmtc)
X*TTI
DU URLLC
DU(Embb)
DU(MMTC)
RLC/MAC
TE
,,

## Slide 13: PRB Estimation Algorithm
Processing at DU(URLLC)
  Derive an estimate for the per TTI arrivals for the following X using geometric smoothing
    = (1-⍺)* + ⍺* , URLLC, MMTC, Embb} , 0 1,
    A different method can used for predicting the arrival demand in place of geometric smoothing
  For system URLLC, MMTC, Embb} , do a system recursion:
    for 0 -1, with =
      =( - )+ ,
  The PRB distribution is based on
  If (=URLLC), then = +
    One approach to set is to use the historical deficit:
      =
      = max( ((n-1)) 0 -1, this can be locally computed at the DU(URLLC), is the actual demand at (n-1)th and ith TTI.
      = max(maxk ((), ) 1 k L, 0 -1, n>L
  Allocate per TTI PRBs, for the following interval (n+1)th TTIs using , as per the slice policy requirements.
    Steps S4 and S5 of the algorithm follows this, setting (URLLC) = , (Embb) = , (MMTC) =
    After steps S4 & S5 is determined

## Slide 14: Algorithm Enhancement (1) – Using Arrival Vectors
The previous demand estimation is calculated based on the nth average arrival traffic over past TTIs and historical average
Instead, a granular estimate of the arrival can be considered in each TTI to account for periodic or correlated arrivals in each TTI
Instead of a vector 1 is communicated from , i.e. { }
The arrival estimation for nth is modified as follows:
  = (1-⍺)* + ⍺*, 1 and URLLC, MMTC, Embb}
For system , URLLC, MMTC, Embb} compute recursively
  =( - )+ + , 0 -1, with =
  The PRB distribution is based on
If (=URLLC), then = + Determined as follows:
  =
  = max( maxi(-+), (n-1)) 0 -1, this can be locally computed at the DU(URLLC), is the actual demand at (n-1)th and ith TTI.
  = max(maxk (maxi(-+)), ) 1 k L, 0 -1, n>L
Allocate per TTI PRBs, for the following interval (n+1)th TTIs using , as per the slice policy requirements
n

## Slide 15: Algorithm Enhancement (2): Vector Allocation using Vector Arrivals
If Allocations are per TTI, we assume the knowledge of {, }
For system , URLLC, MMTC, Embb} ,compute recursively
  For 0 -1, with =
    =( - (n))+ + ,
  For 0 -1 , with = and (n+1) =
    =( - (n+1))+ + ,
  The PRB distribution is based on
// The Burst can be modified according to allocation per TTI
If (=URLLC), then = + , Determined as follows :
  =
  = max( maxi(-+), (n-1)) 0 -1,
  = max(maxk (maxi(-+)), ) 1 k L, 0 -1, n>L
Allocate per TTI PRBs, for the following interval (n+1)th TTIs using , as per the slice policy requirements
n
n+1
n+1
n+2

## Slide 16: Considering DU System Utility
In addition to Arrival and Buffer statistics, the utility parameter defines the satisfaction of the demand for allocation -1) in instance (n-1).
Utility function is known for DU(Embb), DU(MMTC), function of the deficit
One way communicate fairness is using the max deficit, (n)= , 1
Once the deficit statistics is known, it can be used to modify the policy rate, that is used when the systems are over subscribed
Use the deficit Utility to shape the slice policy estimate for PRBp(DU(x)) (x {EMBB and MMTC} ), used in Step 5 :-
  Exponentially average (n) for each update
  Slice Policy update : -
    If (n) > T + delta
      PRBp(DU(x), n) = PRBp(DU(x), n-1) + f((step_size)x U’D(x)((n))) ,( f() maps the (Slope X step-size) to number of incremental PRB)
    If (n)< T – delta
      PRBp(DU(x), n) = PRBp(DU(x), n-1) – f((step_size)x U’D(x)((n))) ,
DU URLLC
DU 1
DU 2
Slice RM
,
,
U(Du(x), d)
Deficit(d)
--> Increasing deficit in each TTI in a DU results in increase of the loss function
T

## Slide 17: Simulations

## Slide 18: Simulation Objectives
RAN with a eNodeB with two schedulars, and serving two set of UEs – Embb and URLLC
Each Schedular serves Embb and other URLLC
A RB management entity that takes in Arrival and Buffer statistics every X TTI and returns the PRB allocation for the following X TTIs
The objective is to study the system under oversubscribed conditions to meet URLLC delay and PER requirements considering retransmissions.
For EMBB users, the quantification is w.r.t loss in throughput with increasing URLLC load
Embb Schedular
URLLC Schedular
RB Slice Mgmt.
PHY
Embb Sources
URLLC sources
CQI(u)
CQI(u)
MAC
RLC
Traffic Stats.

## Slide 19: Traffic Model
Embb can assume a full buffer CBR streamed traffic
  For now CBR for both EMBB and URLLC
Sporadic, poisson arrival with mean arrival rate of for each user .
  URLCC Load is increased by varying packet size e.g. 50-200B or increasing

## Slide 20: Simulation Settings
Single/Multi-cell network with randomly spread Embb and URLLC users
  Static and Mobile
LTE/5G PHY layer settings
  5g features such as , Variable timeslots/TTI , TDD configuration available with mmWave module
URLLC Minislot scheduling
  NS-3 doesn’t have this yet

## Slide 21: Benchmarking and Performance
Benchmarking
  Dynamic URLLC/EMBB Joint Scheduling, using a single schedular
  Disjoint scheduling based on the proposed algorithm
    Static
    Semi-static - with large TTIs
    Dynamic – with Smaller TTIs
Performance
  Embb throughtput
  URLLC Delay CDF
    Required performance is P(Delay <) = 1-
    URLLC RAN Delay target ~9ms, and PER ~ 10-4

## Slide 22: NS-3 LTE Module Changes
LteEnbMac
FfMacUrllcScheduler
FfMacScheduler(Embb)
LteFfrAlgorithm
LteFfrAlgorithm
EnodebRRC
LteEnbPhy
SliceRB Manager
Have the two schedular basic framework up
  URLLC RLC buffer stats and CQI goes Urllc Schdular
  Embb RLC buffer stats and CQI goes Embb Schdular
  RB Manager hasn’t been implemented yet
Userplane
MAC TM

## Slide 23: NS-3 LTE SW

## Slide 24: NS-/5G mmWave Module
Ref: https://par.nsf.gov/servlets/purl/10112885
Channel Modelling:
mmWave Propagation Loss- 3gpp/Tracing/Mathlab, LOS/NLOS, Outdoor/Indoor Model
MIMO
Beamforming
HARQ
RoundRobin/PF/EDF/Max Rate

## Slide 25: Simulation Parameters
Embb/Urllc Scheduler "ns3::PfFfMacScheduler"
PathlossModel "ns3::FriisSpectrumPropagationLossModel"
FadingModel : No
Mobility Model : Constant Position
ns3::LteHelper::UsePdschForCqiGeneration=[true]
ns3::LteHelper::NumberOfComponentCarriers=[1]
# of UEs : 2
TTI : 1ms
Simulation time : 2s
UlBandwidth "25" (RBs)/5Mhz
DlBandwidth "25" (RBs)/5Mhz
DlEarfcn "100"
UlEarfcn "18100"
UeTxPower "10dbm"
UeNoiseFigure "9db"
EnbTxPower "30dbm"
EnbNoiseFigure "5db"

## Slide 26: Simulation Topology
Server
PGw
SGw
EnodeB
Embb UE
Urllc UE

## Slide 27: Results

## Slide 28: RBG Control Function
V
MAC
RLC
ExecuteRBManagement
(UE Traffic Statics, X*TTI, Embb Policy Resv.){ Smoothing/Prediction/RB distribution; returns RB-Allocation}
DoScheduleDlTriggerReq()
URLLCBlockedRBG
URLLC Schedular
DoScheduleDlTriggerReq()
EmbbBlockedRBGs
Embb Schedular
UE-1 flow
UE-2 flow
…
Real time UE Buffer Stats
PHY
ReportBufferUpdate()
SchedulingTrigger/TTI
SetBlockedRbgs()
SetBlockedRbgs()
ReadBlockedRbgs()
ReadBlockedRbgs()
Data
DoSchedDlConfigInd()
SchedDlCqiInfoReq()

## Slide 29: Simulation Settings
RB Control Frequency : {10, 5} TTIs
Exponential averaging time-window parameter : 99, alpha ~ 0.989
Minimum Embb Policy Rbg Size : {0, 1, 3}
Traffic : Full Buffer Model

## Slide 30: Case 1 : Congested Mode, with Embb Policy Reservation =0
CBR URLLC + CBR EMBB >> Cell capacity
RB Control Frequency : 5 TTIs
Embb Policy Reservation =0
URLLC Througput ~[16] Mbps
Embb Throughput ~[0 Mbps]
RBG allocation for URLLC ~ [12]
RBG Allocation for Embb ~[0]
Max Embb HOL Delay :Unbounded
Max URLLC HOL Delay ~[4]ns
-> Embb UE is not receiving data, so no data points

## Slide 31: Case 1(a) : Congested Mode, with Embb Policy Reservation =2
CBR URLLC + CBR EMBB >> Cell capacity
RB Control Frequency : 5 TTIs
Embb Policy Reservation =2
URLLC Througput ~[14] Mbps
Embb Throughput ~[2.5 Mbps]
RBG allocation for URLLC ~ [10]
RBG Allocation for Embb ~[2]
Max Embb HOL Delay :25ns
Max URLLC HOL Delay ~[5]ns

## Slide 32: Case 1: Un-congested Mode
CBR URLLC + CBR EMBB ~= Cell capacity
RB Control Frequency : 5 TTIs
Embb Policy Reservation =0
URLLC Througput ~[16] Mbps
Embb Throughput ~[0 Mbps]
RBG allocation for URLLC ~ [12]
RBG Allocation for Embb ~[0]
Max Embb HOL Delay :Unbounded
Max URLLC HOL Delay ~[4]ns

## Slide 33: Changing the periodicity of RB Mgmt. execution.
CBR URLLC + CBR EMBB ~= Cell capacity
RB Control Frequency : 5 TTIs
Embb Policy Reservation =0
URLLC Througput ~[16] Mbps
Embb Throughput ~[0 Mbps]
RBG allocation for URLLC ~ [12]
RBG Allocation for Embb ~[0]
Max Embb HOL Delay :Unbounded
Max URLLC HOL Delay ~[4]ns

## Slide 34: RB Distribution every 5*TTI RB, and Embb Resv. =0
Full Buffer Model
RB Control Frequency : 5 TTIs
Embb Policy Reservation =0
URLLC Througput ~[0] Mbps
Embb Throughput ~[16 Mbps]
RBG allocation for URLLC ~ [12]
RBG Allocation for Embb ~[0]
Max Embb HOL Delay :Unbounded
Max URLLC HOL Delay ~[0]ns

## Slide 35
Full Buffer Model
RB Control Frequency : 10 TTIs
Embb Policy Reservation =0
URLLC Througput ~[9-15] Mbps
Embb Throughput ~[1-8Mbps]
RBG allocation for URLLC ~ [5,12]
RBG Allocation for Embb ~[0,7]
Max Embb HOL Delay ~[8- 17] ns
Max URLLC HOL Delay ~[0-10]ns
The performance is sensitive to the frequency of executing the RB distribution algorithm
Possible reason :
  Longer TTI duration allows the URLLC queue to drain fast enough to allow residual RBGs to be given to Embb for transmission.
  Smaller TTI control also reduces the HOL delay for URLLC, which is desirable

## Slide 36
Full Buffer Model
RB Control Frequency : 10 TTIs
Embb Policy Reservation =3
URLLC Througput ~[12-13] Mbps
Embb Throughput ~[4-5Mbps]
RBG allocation for URLLC ~ [9]
RBG Allocation for Embb ~[3]
Max Embb HOL Delay ~[16-18] ns
Max URLLC HOL Delay ~[4-6]ns
With reservation, decreasing to 5*TTIs doesn’t change the allocation or the rate

## Slide 37: 10xTTI and With Resv=1
Longer TTI and lower reservation for Embb flows results in more throughput variation (similar to Slide 31), hence higher HOL delays.

## Slide 38: Next Steps
Regenerate graphs, delay CDFs
Change the URLLC traffic model
Code to track the PDCP level packet delay and the CDF
More Cells and UEs, with mobility and HARQ
Benchmarking against Joint scheduling – haven’t seen this feature in NS-3 yet
  We could implement it..